## Slide 1: Improvement on LEACH Protocol of Wireless Sensor Network
Multihop LEACH
Energy LEACH

## Slide 2: Abstract
Energy-LEACH and multihop –LEACH protocols.
Energy-LEACH protocol improves the choice method of the cluster head,
  makes some nodes which have more residual energy as cluster heads in next round.
Multihop-LEACH protocol improves communication mode
  from single hop to multi-hop between cluster head and sink.
Simulation results show that
  energy-LEACH and multihop-LEACH protocols have better performance than LEACH protocols.

## Slide 3: Introduction
WSN consists of a certain number of smart sensors which form a multihop Ad Hoc network by radio communications in sensor field.
WSN aims to perceive in collaborative mode, gather , deal with and send information to observer in network areas.
Three factors of WSN
  Sensor
  sensing object
  observer
WSN protocol stack contains
  physical layer
  data link layer
  network layer
  transport layer
  application layer
According to network architecture, routing protocols classification
  plane routing
  grade routing
  position routing

## Slide 4: Introduction (cont…)
LEACH (Lower Energy Adaptive Clustering Hierarchy) protocol is a grade routing protocol.
  LEACH protocols is already discussed in detail.
Sun limin, et. al., and W. Heinzelman, et. al., modified leach protocol, but it is still faulty and the performance matrixes are complex.
In this paper, a new modified energy-LEACH protocol is presented which designs in detail and improves the wang wei, leach protocol with the help of two simple performance matrixes.
Multi-hop protocol introduced by Mo Xiaoyan; is quite complex.
Multihop-LEACH protocol introduced in this paper is :
  Simple
  Great performance
  Especially fit for WSN with restrictive energy.

## Slide 5: LEACH protocol
Main techniques of LEACH protocol include algorithms for:
  distributing cluster forming
  adaptive cluster forming
  cluster header position changing
The technique of distributing cluster forming ensures self-organization of most target nodes.
The adaptive cluster forming and cluster header position changing algorithms ensure
  to share the energy dissipation fairly among all nodes and prolong the lifetime of the whole system in the end.

## Slide 6: Description of LEACH protocol
LEACH protocol provides a concept of rounds.
Each round contains two states:
  cluster setup state
  steady state.
In cluster setup state
  forms cluster in self-adaptive mode;
In steady state,
  transfers data.
The time of transfer state is usually longer than the time of set up state for saving the protocol payload.

## Slide 7: Operation Time of LEACH

## Slide 8: Flow chart of LEACH protocol

## Slide 9: Cluster Formation of LEACH protocol

## Slide 10: Different Processes of LEACH protocol

## Slide 11: Improvements of LEACH protocol
The criterion of selecting cluster head node
Multi-hop communication among cluster heads

## Slide 12: The criterion of selecting cluster head node
LEACH protocol randomly selects cluster head at each round.
  Therefore, some nodes maybe exhaust energy too quickly due to being selected as cluster head many times.
Our modified protocol makes the nodes with more residual energy have more chance as cluster head
  prevent the whole network to die too early.

## Slide 13: Multi-hop communication among cluster heads
Cluster heads directly communicate with sink in LEACH protocol.
  The energy consumption between cluster head and sink are greater than energy consumption among cluster heads, so the cluster head will exhaust energy soon.
Multi-hop communication
  can avoid the whole network from dying quickly
  prolong the network lifetime by balancing the energy consumption among the network.

## Slide 14: Energy-LEACH protocol
Energy-LEACH protocol improves the cluster head selection procedure.
  It makes residual energy of node as the main matrix which decides
    whether these nodes turn into cluster head or not in the next round.
In first round communication, every node has the same probability to turn into cluster head.
n (n=p×N) nodes are randomly selected as cluster heads, and then, the residual energy of each node is different after one round communication.
We select n nodes with more residual energy as cluster heads in next round communication, and so on until all nodes are dead.

## Slide 15: Energy-LEACH protocol(Conti…)
Same as the LEACH protocol, energy-LEACH protocol also divides into many rounds,
Each round contains following two phases
  cluster formation phase (Set up phase)
  cluster steady phase

## Slide 16: 2.3. Energy-LEACH protocol
In cluster formation phase,
  each node decides whether to turn into cluster head or not by comparing with residual energy；
    Some nodes with more residual energy turn into cluster heads
      send cluster head information to inform other nodes.
    The other nodes with less residual energy turn into common nodes,
      send information about joining cluster to a cluster head；

## Slide 17: Flow chart of Energy-LEACH protocol
In cluster formation phase,
the flow chart of whether a node turns into cluster head or a common node is shown in figure

## Slide 18: Cluster Steady Phase of E-LEACH protocol
In cluster steady phase,
  nodes in a cluster send data according to TDMA table, and cluster heads receive, fuse and send data to sink.
  After a period of time, the network reforms the cluster head selection procedure in a new round.

## Slide 19: Multihop-LEACH protocol
Why we Introduce M-LEACH?
  Each cluster head directly communicates with sink
    no matter the distance between cluster head and sink is far or near in LEACH protocol.
    It will consume lot of energy if the distance is far.
A further modified LEACH protocol (multihop-LEACH protocol)
  which selects optimal path and adopts multihop between cluster head and sink is presented here.
    First, multi-hop communication is adopted among cluster heads.
    Then, according to the selected optimal path,
      these cluster heads transmit data to the corresponding cluster head which is nearest to sink.
    Finally, this cluster head sends data to sink.

## Slide 20: Multihop-LEACH protocol
Multihop-LEACH protocol is almost the same as LEACH protocol,
  only makes communication mode from single hop to multi-hop between cluster heads and sink.
  Its multi-hop routing algorithm within one round is shown in figure.
Routing of multihop-LEACH protocol

## Slide 21: Simulation analysis
Performances Comparison of
  LEACH protocol
  energy-LEACH protocol
  multihop-LEACH protocol

## Slide 22: Performance matrixes
Network lifetime of WSN is very important due to restricting energy.
Here, two matrixes are given to show the state of network energy consumption.
  Residual energy of all node;
    shows all residual energy of 100 node
  Time of network death for different number of nodes.
    time when the whole network is finally dead under the condition of a given number of node.

## Slide 23: Simulation parameters setting
Sensor nodes contain two kinds of nodes:
  sink nodes (no energy restriction)
  common nodes (with energy restriction);
Nodes are randomly distributed in a area within 80m×80m,
  and the efficient distance among nodes is 15m;
Suppose that every node knows its position, channels between sensor nodes are ideal, sending energy consumption is the same as receiving energy consumption,
  energy consumption in each round is 0.05J, and initial energy of each node is 10J;
Energy consumption between cluster head and sink is 59 times of the energy consumption among common nodes;
Probability of being cluster head equals 0.04;
Each node sends data in every 0.5s, and sends data in every time interval at a random time by a TDMA slotted MAC protocol;

## Slide 24: Simulation parameters setting
7. Network with same number of nodes still may have different performance due to network structure.
In our simulation, the network topology is randomly built each time, and simulation results are averaged for 3 different network topologies.

## Slide 25: Simulation results
Figure shows the performance of residual energy of LEACH protocol, our energy-LEACH protocol and multihop-LEACH protocol.
Multihop-LEACH protocol has more residual energy than LEACH and energy-LEACH protocols.
Energy-LEACH protocol has the same residual energy as LEACH protocol in the beginning,
  but Energy-LEACH protocol gradually has more residual energy than LEACH protocol after a certain period of time (120s for our simulation).
Figure: Residual energy of three protocols
with 100 nodes

## Slide 26: Simulation results
Figure shows the performance of network death time for different number of nodes.
  Multihop-LEACH protocol survives longer than both energy-LEACH protocol and LEACH protocol
  Energy-LEACH protocol survives longer than LEACH protocol.
  The results show that
    our two modified protocols prolong the network lifetime as compared with the commonly used LEACH protocol.
Figure: Time of network death in different num of
node of three protocols

## Slide 27: Conclusion
Two modified LEACH protocols: energy-LEACH protocol and multihop-LEACH protocol are presented in this paper.
  Energy-LEACH protocol considers residual energy in the phase of cluster head selection.
  Multihop-LEACH protocol adopts multi-hop communication between cluster and sink.
Simulation results show that
  Energy-LEACH and multihop- LEACH protocols have better performance than LEACH protocol.